# Office of the Vice President for Research

Environmental Health & Safety

CHANGES HAVE BEEN MADE TO THE UNIVERSITY’S ENERGIZED ELECTRICAL WORK PERMIT TO REFLECT UPDATED INFORMATION IN NFPA 70E - EDITION 2012.

Summary of Revisions to Energized Electrical Work Permit - October 2013

- Revision date for permit has changed from 03/10 to 10/’13.

- The Table designation in Permit section III for Protective Boundaries and class rating for insulating equipment and tools is now Table 130.4(C)(a).

- The Table designation in Permit section IV for Hazard Rating and Protective Boundaries  is now Table 130.7(C)(15)(a).

- Information in Permit section IV - Arc Flash Boundary has been updated with designated sections in NFPA 70 ed.’12 on arc flash boundaries.

- Additional information has been added at the end of Permit section IV to review Notes (1) through (6) at end of Table 130.7(C)(15)(a).

- Table 130.7(C)(16) Protective Clothing has been added in Section IV.  This is a reference for arc rated clothing and personal protective equipment required for Hazard Risk Categories 0 through 4.

- The classes of Electrical Hard Hat have been defined in section IV-Hazard risk Category 1.  The hard hat classes are required for Hazard risk Category 2, 3 &4.

- Hazard Risk Category *2 in the 2009 edition has been omitted.  The 2012 edition now requires donning a balaclava sock hood underneath an arc rated face shield that provides full covering of the forehead and neck for Hazard Risk Category 2.